## Slide 1: Architecture of Microprocessors Case Study: 8085

## Slide 3
8085/8086
8254 (Timer)
8257 (DMA
Controller)
MICROPROCESSOR Based Development Board
8251 (USART)
8255 (Parallel interface)

## Slide 4: What is a Microprocessor Based System?
Microcomputer is a microprocessor based system.
Includes :
      Microprocessor
      Input/Output
      Memory
Components are connected through a communication path called a bus
How we can differentiate microcomputer and a microprocessor?
    uP is one component of the microcomputer
    The CPU functions of the microcomputer are performed by the uP
The term peripherals is used for I/O devices.

## Slide 5: uP based System Architecture with Bus Architecture

## Slide 6: What is a microprocessor?
Microprocessor :-
    multipurpose,
    programmable,
    clock driven,
    register-based electronic device
    that reads binary instruction from a storage device called memory,
    accepts binary data as input and
    process data according to the instructions, and
    provides results as output.
  Manufactured by using LSI or VLSI
  Microprocessor operation is similar to human brain
How we can differentiate CPU & uP ?
  CPU is implemented on one or more circuit boards to perform the computing functions
  uP is similar to CPU
  uP - CPU on a single chip

## Slide 7: Main 3 segments of uP
  ALU :- This area of uP will perform various computing functions such as arithmetic operations (Addition & Subtraction) and logic operations (AND/OR/EXOR)
  Register Array :- This area of uP consists of various register; B,C,D,E,H & L. Store data temporarily during execution of a program and are accessible to the user through instruction
  Control Unit :- Provides necessary timing and control signals to all the operations. Controls the flow of data b/w uP and memory and peripherals.

## Slide 8: Memory
  Memory stores binary information as instruction and data
  2 sections
    Read only Memory (ROM)
      Program in ROM can only be read, not altered.
      Store programs that don’t need alteration
    Read/Write Memory (RAM)
      User Memory
      Stores user program & data
      Information stored can be easily read and altered
Consider the monitor program, generally stored in ROM
    This program interprets the information entered through a keyboard and provides equivalent binary to the uP.
    The monitor programs monitors the Hex Key and stores data in R/W memory

## Slide 9: Input/ Output & System Bus
Input/Output :-
  Also known as peripherals
  Communicating with the outside world through I/O
  Inputs devices :- keyboard, switches, ADC
    Transfer binary information from outside world to the uP
  Output devices:- LED, CRT, Video screen (monitor), XY Plotter, Magnetic Tape, DAC
    Transfer data from uP to the outside world
System Bus:-
  Communication path between the uP and peripherals
  Bus - Group of wires to carry bits
  All peripherals share the same bus
  uP communicates with only one peripheral at a time
  Timing is provided by the CU of the uP.

## Slide 10: How does a uP works?
  Fetch, Decode, Execute
    uP fetches the first instruction from the memory
    Decodes it
    Execute the instruction
  Uses the system bus to fetch the instruction and data from the memory in the entire process
  Uses registers to store data temporarily
  Performs the computing function in the ALU
  Sends out the result in binary using the same bus lines to the o/p.

## Slide 11: Terminology
Word :- No: of bits uP recognizes and process at a time
Machine Language:-
  uP communicates and operates in 0’s & 1’s
  For communication, give the instruction in binary language
Assembly language
  Programmer writes the program in words
  Symbolic code for each instruction, called mnemonics
Assembler :-
  Program that translates the mnemonics entered from the keyboard into the corresponding binary machine codes of the uP

## Slide 12: INTEL 8085-Features
It is an 8 bit general purpose microprocessor.
It is a single chip N-MOS device with 40 pins.
Capable for addressing 64K of memory
It has multiplexed address and data bus.(AD0-AD7).
It works on 5 Volt dc power supply.
The maximum clock frequency is 3 MHz - (8085A-5MHz)
It provides 74 instructions with 5 different addressing modes.

## Slide 13
Signals can be classified into 6 groups:
  Address Bus
  Data Bus
  Control and Status signals
  Power supply and frequency signals
  Externally initiated signals
  Serial I/O ports

## Slide 14
Address Bus
  16 address lines
  A15 – A8 & AD7 – AD0
  A15 – A8 are unidirectional, called high order address
  AD7 – AD0 for dual purpose
Multiplexed Address/Data Bus
  AD7-AD0 are bidirectional
  Low order address bus or data bus
  Earlier part of cycle, acts as low order address bus
  Later part, acts as data bus
Control & Status Signal
  2 control signals (RD & WR)
  3 Status signals (IO/M, S1 & S0)
  1 Special Signal (ALE)
Power Supply and Clock Frequency
      Vcc - +5V power supply
      Vss – Ground Reference
      X1and X2 are the inputs from the crystal or clock generating circuit.
        The frequency is internally divided by 2.
        So, to run the microprocessor at 3 MHz, a clock running at 6 MHz should be connected to the X1 and X2 pins. (Crystal of 6MHz frequency should be connected)
      CLK OUT – Clock Output
        An output clock pin to drive the clock of the rest of the system.
Externally Initiated Signals
      Includes 5 Interrupt signals
          INTR, INTA, RST 7.5, RST 6.5, RST 5.5, TRAP
      3 DMA (Direct memory Access) Controller signals
          HOLD, HLDA, READY
      RESET IN
      RESET OUT
Serial I/O Ports
    SID – Serial Input Transmission
    SOD – Serial Output Transmission

## Slide 15: 8085 Models
Hardware Model (physical electronics components)
Programming Model (information needed to write program)

## Slide 16
8085 Hardware Model
2 major segments
  Segment 1
    ALU
    8-bit Accumulator
    Instruction Decoder
    Flags
  Segment 2
    8-bit & 16 bit Register

## Slide 17: 8085 Programming Model
Includes some segments of ALU and registers
Includes information critical for writing assembly language
6 GPR
1 Accumulator
1 Flag register
16-bit Program Counter
16-bit Stack Pointer

## Slide 18: Program Counter
16–bit register hold memory address
PC is used to sequence the execution of the instruction
Function of PC is to point to the memory address from which the next byte is to be fetched
When a byte (machine code) is being fetched, the program counter is incremented by one to point to the next memory location
16-bit register used as a memory pointer
It points to a memory location in R/W memory, called the stack
The beginning of the stack is defined by loading 16-bit address in the stack pointer.
The stack is the sequence of memory locations defined by the programmer.
The stack is used to save the content of a register during the execution of the program.
Stack Pointer

## Slide 19: 8085 Architecture
        ALU
        Timing & Control Unit
        Instruction Register and Decoder
        Register Array
        Interrupt Control
        Serial I/O Control

## Slide 20
Aum Amriteswaryai Namah:
8085 ARCHITECTURE
Interrupt Control
Serial I/O Control
Accumulator
(8)
Timing and Control
CLK
GEN Control Status DMA Reset
Instruction
Reg.(8)
Multiplexer
W (8)
Temp.Reg.
Z (8)
Temp.Reg.
C Reg.(8)
B Reg.(8)
D Reg.(8)
E Reg.(8)
H Reg.(8)
L Reg.(8)
Stack Pointer(16)
Program Counter(16)
Incrementer/Decrementer Address Latch (16)
Address
Buffer (8)
Data/Address Buffer(8)
Instruction Decoder and Machine Cycle Encoder
A15 - A8
(Address Bus)
AD7 – AD0
(Address/Data Bus)
Reg.Select
Temp.Reg
(8)
Flag
Flip-Flops(5)
A L
U
(8)
INTR
INTA
RST5.5
RST6.5
RST7.5
TRAP
SID
SOD
X2
X1
CLK OUT
Ready
RD
WR
ALE
S0
S1
IO/M
HOLD
HLDA
Reset IN
Reset OUT
Power Supply +5v
Ground
8 bit Internal Data Bus

## Slide 21: ALU (ARITHMETIC AND LOGICAL UNIT)
It is referred to be as ALU which acts as a backbone for any arithmetic and logical operation as addition, subtraction, division, multiplication, AND, OR, NOT etc.
Once the operation is performed, the result will be stored in accumulator, which is again a register.

## Slide 22: Timing and Control Unit
Instruction register is a temporary storage area for the current instruction before it is being executed.
Instruction fetched from memory is loaded into IR
Decoder decodes the instruction & establishes the sequence of events to follow
Not programmable & cannot accessed through any instruction
Decoded instruction will be then moved to the next stage
Synchronizes all the uP operation with the clock
Generates control signal necessary for the communication between uP and peripherals
Instruction Register and Decoder

## Slide 23: ACCUMULATOR
Most important component of the entire Mu-P. 8 bit register.
It is inevitable in all the arithmetic and logical operations since the result is going to be stored in this register.
It is represented by the character A.
When there is a new 8 bit data entering, the previously stored data will get automatically over written.
Any operation that is happening will happen through Accumulator register only.
Without Accumulator, Nothing would happen

## Slide 24: Flag Register
S | Z | X | AC | X | P | X | CY

## Slide 25: BUS STRUCTURE IN 8085
What a bus is?
A bus is as simple as the bus that people travel with. What is it meant for?
It takes people and freight from a place to another.
Same is the case here with microprocessor.
Microprocessor often needs to send lot of control signals, data etc. to the peripherals and devices connected to it.
All those are carried via the bus. In short it is the medium.

## Slide 26: Address Bus
Address bus
As the name indicates it is used to carry the address.
8085 has 16 address lines which means it can have 2^16 = 65536bytes memory locations.
The address bus will be mainly used to recognize a memory location or a connected peripheral.
Postman basically delivers the letters using address. Likewise it is mandatory to have the identity for the memory locations and it is referred to be as an address.
Address bus is always unidirectional. The communication happens from microprocessor to the peripherals

## Slide 27: Data Bus
Data bus
This is bidirectional wires which carries data from to Microprocessor.
Any information that gets in or goes out of Microprocessor is through the data bus only.
There are 8 data lines from D0 to D7 as and this is the reason why we call it an 8 bit processor.
Data bus is used to carry the instructions, results of the operations etc. to the peripherals and memory unit.
When we quote that it is an 8 bit processor, it implies that the large data chunk has to be broken into smaller ones of up to 255 (o to 255, 28 )

## Slide 28: Control Bus
Control bus
All the controlling actions are carried out through these lines.
It can be unidirectional or bidirectional.
The control signals will intimate the microprocessor on where to read or where to write.
Many control signals are available with 8085.
All of them are discussed in detail when the pin description of 8085 is handled. Reader has to wait till then.

## Slide 29: Processor Cycles
Instruction Cycle:
The sequence of operations that a processor has to carry out while executing the instruction is called instruction cycle.
Machine Cycle:
Each instruction cycle of a processor consist of a number of basic operations called machine cycles or processor cycles.
Instruction Cycle
Fetch Cycle
Execute Cycle

## Slide 30: T States
The time taken by the processor to execute a machine cycle is expressed in T - States.
One T – state is equal to the time period of the internal clock signal of the processor.
The T- state starts at the falling edge of a clock.

## Slide 31: Thank You

## Slide 32
Aum Amriteswaryai Namah:
PIN DIAGRAM
8085
1
2
3
4
5
6
7
8
10
9
11
12
13
14
15
16
17
18
20
19
40
39
38
37
36
35
34
33
31
32
30
29
28
27
26
25
24
23
21
22
X1
Vss
X2
RESET OUT
SOD
SID
TRAP
RST 7.5
RST 5.5
RST 6.5
INTR
INTA
AD0
AD1
AD2
AD3
AD4
AD5
AD6
AD7
Vcc
HOLD
HLDA
CLK(OUT)
RESET IN
READY
IO/M
S1
RD
WR
ALE
S0
A15
A14
A13
A12
A11
A10
A9
A8