## Slide 1: 19CSE301 COMPUTER NETWORKS

## Slide 2: Syllabus- 19CSE301 Computer Networks-3-0-3 4
Unit 1
The Internet-The Network Edge, the Network Core, Delay, Loss, and Throughput in Packet Switched Networks, Protocol Layers and Their Service Models. Principles of Network Applications: The Web and HTTP, File Trans- fer: FTP, Electronic Mail in the Internet, DNS - The Internet’s Directory Service, Peer-to-Peer Applications. Introduction and Transport Layer Services: Multiplexing and Demultiplexing, Connectionless Transport - UDP, Principles of Reliable Data Transfer.
Unit 2
Transport layer - Connection Oriented Transport - TCP, Principles of Congestion Control, TCP Congestion Control. Introduction Network Layer: Virtual Circuit and Datagram Networks, Inside a Router, The Inter- net Protocol (IP) - Forwarding and Addressing in the Internet, Routing Algorithms, Routing in the Internet, Broadcast and Multicast Routing.
Unit 3
The Link Layer and Local Area Networks - Introduction and Services, Error-Detection and Correction Tech- niques, Multiple Access Protocols, Link-Layer Addressing, Ethernet, Link-Layer Switches, Case study – Virtualization and Data center networking.
Text Books
1. Kurose J F and Ross K W, “Computer Networking: A Top-Down Approach”, Sixth Edition, Pearson Press, 2013.
References
Tanenbaum A S, “Computer Networks”, Third Edition, PHI, 2004.
Stallings W, “Data and Computer Communications”, Seventh Edition, Pearson Education Asia, 2004.

## Slide 4: Chapters
Chapter 1 Computer Networks and the Internet
Chapter 2 Application Layer
Chapter 3 Transport Layer
Chapter 4 The Network Layer
Chapter 5 The Link Layer and LANs

## Slide 5: Evaluation Pattern
Computer Networks Theory
Class Test(2 test , 5 marks each) - 10 marks
Dated Notebook submission - 5 marks
Computer Networks Lab
Lab Assignment Submission(wireshark) - 5 marks
Socket Programming(project) - 10 marks
End Lab exam (Packet Tracer) - 15 marks

## Slide 6
Chapter I:
Computer Networks and the Internet

## Slide 7: Chapter -1 Introduction
1.1 What Is the Internet?
  1.1.3 What Is a Protocol?
1.2 The Network Edge
  1.2.1 Access Networks
  1.2.2 Physical Media
1.3 The Network Core
  1.3.1 Packet Switching
  1.3.2 Circuit Switching
1.3.3 A Network of Networks
1.4 Delay, Loss, and Throughput in Packet-Switched Networks
1.5 Protocol Layers and Their Service Models
  1.5.1 Layered Architecture
  1.5.2 Encapsulation

## Slide 8: What is a computer Network
A computer network is a set of computers that are connected together so that they can share information .Computer networks are the basis of communication in IT. They are used in a huge variety of ways and can include many different types of network..
Some of the things that networks are used for include:
  Communicating using email, video, instant messaging and other methods
  Sharing devices such as printers, scanners and photocopiers
  Sharing files
  Sharing software and operating programs on remote systems
  Allowing network users to easily access and maintain information

## Slide 10: What is a Computer Network?
A set of communication elements connected by communication links
➭ Communication elements
  Computers, printers, mobile phones, …
  Routers, switches, ...
➭ Communication links
  optic fiber
  coaxial cable
  twisted pair
  wireless (radio, microwave, satellite)
➭ Topologies
Ring, Star, Bus, Tree, Mesh
local ISP
company network
regional ISP
router
workstation
mobile
server

## Slide 11: Introduction
11
Computer Network
  an interconnected collection of autonomous computers
Internet: “network of networks”
    loosely hierarchical
    public Internet versus private Intranet
WWW a distributed systems run on the top of Internet
Distributed System
  High degree of cohesiveness and transparency
  A software system built on top of a network

## Slide 12: Internetworks
A gateway is a node (router) in a computer network, a key stopping point for data on its way to or from other networks.
... For basic Internet connections at home, the gateway is the Internet Service Provider that gives you access to the
entire Internet.
12
Internetworks connect networks with different hardware and software
A collection of interconnected networks is called an internetwork or internet
Gateways are used to make the connection and to provide the necessary translation (protocol conversion)

## Slide 13: Internet : WWW
World Wide Web, ( Web), is a large distributed system, a collection of websites or web pages stored in web servers and connected to local computers through the internet.
Internet is the network of connected computers that the web works on, as well as what emails and files travel across.
Think of the internet as the roads that connect towns and cities together. The world wide web contains the things you see on
the roads like houses and shops.

## Slide 14: Evolution of Internet

## Slide 15: History of Internet
The first workable prototype of
the Internet came in the late 1960s with the creation of ARPANET, or the Advanced Research Projects Agency Network.
Originally funded by the U.S. Department of Defense, ARPANET used packet switching to allow multiple computers to communicate on a single network.

## Slide 16: Internet – its component
mobile network
global ISP
regional ISP
home
network
institutional
network
J. Kurose and K. Ross 2012, Computer Network,6th ed.
Multiple ISPs together form
the Internet
Global, regional ISPs, residential ISPs, home network, enterprise network
Hosts, servers, Network core, switches, routers

## Slide 17: Internet – its component
mobile network
global ISP
regional ISP
home
network
institutional
network
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP,
Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
Physical media
  Copper wire, optical
fiber,
The IETF is a large open international community of network designers, operators, vendors, and researcher who make the Internet
work better by producing high quality, relevant technical documents that influence the way people design, use, and manage the Internet.